## Slide 1
TA 111 - Engineering Graphics
Lecture 1 – Lines and Letterings (Self-readable material)

## Slide 2
Summary of Presentation
Line
Letterings
Scale

## Slide 3
  ‘Lines’ represent the shape of an object in the form of either an edge, a surface, or contours of the object
  ‘Lettering’ is used to describe the size and other necessary information
  Lines & lettering along with certain symbols, abbreviations, and standard practices collectively make the complete description of an object on an engineering drawing
Lines and Letterings

## Slide 4
Construction-Continuous thin
Object- Continuous thick
Hidden-Dashed line
Center line-Chain thin
Hinge line-Chain thick
Dimension-Arrowed line
Types of Lines

## Slide 5
Front Viewing Direction
Top Viewing Direction
IMPORTANT NOTE:
Object lines and construction lines should always be distinguishable
You may use H for object lines and 2H for construction lines
You should NOT erase the construction lines after drawing (in this course)
Front View
Top View
100
Object Line
Construction Line
Center Line
Hidden Line
Types of Lines in a simple drawing

## Slide 6
Body of small letters = 2/3 of Capital letters
Cap line and Drop line are 1/3 each from waist and Base lines
e.g. Capital letter = 9 mm
Body of small letter = 6 mm
Cap and Drop lines = 3 mm
Atg
Cap Line
Waist Line
Base Line
Drop Line
Letterings
  Lettering: It all starts with A, B, C,.. .1, 2,3… !!!!!
  Guidelines are construction lines
  Light pencil lines – use 2H/H pencil
  For capital letters: Draw only cap line and base line
  For lowercase letters: Draw waist line and drop line also

## Slide 7
Engineering lettering is commonly UPPERCASE
Title Block: 8/6 mm, Dimensions: 6 mm
Each letter is made up of a series of single strokes
Judging by the eye, the distance between the letters should be approximately equal
Letters and Number using H Pencil
Use only CAPITAL LETTERS and NUMBERS
Principles of Letterings

## Slide 8
Legibility: Each letter must be distinct.
Stability: The bottom of letters such as B are larger than the top.
Composition: Each portion of each letter is formed to an exact standard.
Uniformity: All “A’s” are alike, all “B’s are alike, etc.
Alignment: The vertical axes passing through all letters are parallel. No slant!
Principles of Letterings

## Slide 9
ü
û
Stroke the pencil in the acute angle direction. This will save the paper from tearing
Acute Angle Stroking

## Slide 16
USE THIS IN ALL DRAWINGS

## Slide 18
Lettering Practice – Lab + Home

## Slide 19
Drawings made in one country may be used for manufacturing parts or assembly in another country !
Need for STANDARDS !
(BIS, DIN, JIS, ASTM …)
Why take so much trouble?

## Slide 20
Note: Always actual dimension are written on drawings.
Scales e.g.:
1:2, 1:5,1:10, etc.
Note: A drawing should always have the SCALE
Cannot draw all objects on drawing sheet in full size
Scale

## Slide 21
Scale

## Slide 22
5 6 7 8 9 10 12
Some basic geometric shapes

## Slide 23
Cylinders and Cones
Some basic geometric shapes

## Slide 24
THANKS