## Slide 1: Capacity Planning
Achieve match between the long-term supply capabilities of an organization and the predicted level of long-term demand
  Overcapacity: high cost
  Undercapacity: strained resources and possible loss of customers
Key Questions:
  What kind of capacity is needed?
  How much is needed to match demand?
  When is it needed?
Capacity
  The maximum amount that a process can produce in a given unit of time
Process : collection of activities that transforms inputs into outputs that are valuable to the customer
Capacity (process capacity) is the capacity of the bottleneck activity

## Slide 2: Elements of a Process
Activity
Flow
Inventory buffer
Decision point

## Slide 3: Process Flow Diagram
Assemble
Cook
Deliver
RM
Customer order
Burger making

## Slide 4: Process Flow Diagram---Process Capacity
Assemble
Cook
Deliver
RM
Customer order
45 units/hour
Burger making: Scenario 1
Activity time |  | 2 min/unit |  | 3 min/unit |  | 1 min/unit
Number of resources |  | 1 |  | 1 |  | 1
Capacity |  | 30 units/hr |  | 20 units/hr |  | 60 units/hr

## Slide 5: Process Flow Diagram---Demand Constrained System
Assemble
Cook
Deliver
RM
Customer order
45 units/hour
Burger making: Scenario 2
Activity time |  | 2 min/unit |  | 3min/unit |  | 1 min/unit
Number of resources |  | 2 |  | 3 |  | 1
Capacity |  | 60 units/hr |  | 60 units/hr |  | 60 units/hr
Flow rate = demand = 45 units/hour

## Slide 6: Process Flow Diagram---Supply Constrained Process
Assemble
Cook
Deliver
RM
Customer order
45 units/hour
Burger making: Scenario 1
Activity time |  | 2 min/unit |  | 3 min/unit |  | 1 min/unit
Number of resources |  | 1 |  | 1 |  | 1
Capacity |  | 30 units/hr |  | 20 units/hr |  | 60 units/hr
Flow rate = capacity of Assemble stage = 20 units/hour

## Slide 7: Cycle Time and Flow Time
Cycle time = 3 minutes
Flow time = 7 minutes (measured in the steady state)
Burger : Scenario 1

## Slide 8: Process Flow Diagram---Process Capacity
Assemble
Cook
Deliver
RM
Customer order
45 units/hour
Burger: Scenario 3
Activity time |  | 2 min/unit |  | 3 min/unit |  | 1 min/unit
Number of resources |  | 1 |  | 1 |  | 1
Capacity |  | 30 units/hr |  | 20 units/hr |  | 60 units/hr
WIP

## Slide 9: Supply Constrained: Adding Buffer does not Change the Capacity
Cycle time = 3 minutes
Flow time = Increasing
Burger: Scenario 3
Buffer

## Slide 10: Process Analysis

## Slide 11: Process Analysis

## Slide 12: Process Analysis of Circored Plant
Source: Matching supply with demand: An introduction to operations management, Cachon and Terwiesch

## Slide 13
Source: Matching supply with demand: An introduction to operations management, Cachon and Terwiesch

## Slide 14
Source: Matching supply with demand: An introduction to operations management, Cachon and Terwiesch

## Slide 15: Case 1: Unlimited Demand
Process Step | Capacity | Utilization
Preheater | 120 tons/hr | 100/120 = 83.3%
Lock hoppers | 110 tons/hr | 100/110 = 90.9%
First reactor | 112 tons/hr | 100/112 = 89.3%
Second reactor | 100 tons/hr | 100/100 = 100%
Flash heater | 135 tons/hr | 100/135 = 74.1%
Discharger | 118 tons/hr | 100/118 = 84.7%
Briquetting | 165 tons/hr | 100/165 = 60.6%
Flow rate = bottleneck capacity = 100 tons/hr

## Slide 16: Case 2: Demand =125 tons/hr
Process Step | Capacity | Utilization | Implied Utilization
Preheater | 120 tons/hr | 100/120 = 83.3% | 125/120 = 104.2%
Lock hoppers | 110 tons/hr | 100/110 = 90.9% | 125/110 = 113.63%
First reactor | 112 tons/hr | 100/112 = 89.3% | 125/112 = 111.6%
Second reactor | 100 tons/hr | 100/100 = 100% | 125/100 = 125%
Flash heater | 135 tons/hr | 100/135 = 74.1% | 125/135 = 92.6%
Discharger | 118 tons/hr | 100/118 = 84.7% | 125/118 = 105.9%
Briquetting | 165 tons/hr | 100/165 = 60.6% | 125/165 = 75.8%
Flow rate = bottleneck capacity = 100 tons/hr

## Slide 17: Case 3: Demand =80 tons/hr
Process Step | Capacity | (Implied ) Utilization
Preheater | 120 tons/hr | 80/120 = 66.67%
Lock hoppers | 110 tons/hr | 80/110 = 72.72%
First reactor | 112 tons/hr | 80/112 = 71.42%
Second reactor | 100 tons/hr | 80/100 = 80%
Flash heater | 135 tons/hr | 80/135 = 59.25%
Discharger | 118 tons/hr | 80/118 = 67.79%
Briquetting | 165 tons/hr | 80/165 = 48.48%
Flow rate = Min{Demand, Process capacity} = Min{80, 100}= 80 tons/hr